## Slide 1
MUSASHI AUTO PARTS INDIA PVT LIMITEd
No Limitations For Improvements……….
WELCOME
YOU ALL MIQC – 2018-19
HORIZON
Notes: All: First saying NAMASTHE
Sajin: We ARE FROM MUSASHI AUTO PART BLR PLANT. WELCOME YOU ALL FOR THE NH CIRCLE PRESENTATION.
WE ARE TEAM (ALL) HORIZON

## Slide 2
6
5
: HAY Group
: Musashi
EU
9 bases
Asia
16 bases
America
5 bases
30 production bases in global
Global network makes optimal production and
supply system achievable. (30 Affiliates in 13 countries)
GLOBAL NETWORK
MUSASHI AUTO PARTS BENGALURU
Notes: PLANT EXPLAINATION BY SAJIN

## Slide 3
North America
Europe
Asia
South America
Japan
OUR CUSTOMERS
Notes: CUSTOMER INTRODUCTION BY SAJIN

## Slide 4
MOTOR CYCLE TRANSMISSION
SCOOTER TRANSMISSION
ENGINE GEAR
CAM SHAFT
CONNECTING ROD
KICK ASSY
WE WERE IN OPERATION SINCE 2013
PLANT INTRODUCTION
WE MANUFACTURE
OUR FACILITY
GEAR CUTTING
HEAT TREATMENT
FORGING
GRINDING
ASSEMBLY
Notes: SAJIN: We manufacture
MANOHAR: Motorcycle transmission
PRAMOD: Scooter
PRAVEEN: Engine gear
MANOHAR: Cam shaft
PRAMOD: Connecting rod
PRAVEEN: Kick assembly
SAJIN: Our facilities are
MANOHAR: Forging
PRAMOD: Gear cutting
PRAVEEN: Heat treatment
MANOHAR: grinding
PRAMOD: Assy
SAJIN: We were in operation since 2013

## Slide 5
TEAM INTRODUCTION
HORIZON
TOTAL MEMBERS : 6 PERSON
NO OF MEETINGS : 5
TOTAL ATTENDANCE : 91%
SAJIN ( Prod.)
STRENGTH: MACHINING
UDAYKUMAR HOSUR
STRENGTH: GIVING IDEAS
SHIVKUAMR ( PROD )
STRENGTH: PROGRAMMING
ARUN (PROD)
STRENGTH: PART SETTING
VIGNESH (MAINT)
STRENGTH: TOOLING
BHASKAR ( QA)
STRENGTH: SHARING INFORMATION
OUR STRENGTH IS GEAR CUTTING
Notes: SAJIN : TEAM INTRODUCTION OF UDAY SAN AND THE MEETING EXPLAINATION
ALL SELF INTRODUCTION
BHASKAR : MEMBER INTRODUCTION AND SELF

## Slide 6
ACTIVITY SCHEDULE PLANNING
CIRCLE NAME: HORIZON
PROJECT:- TCE REDUCTION
Meeting time every Friday 3 to 4 pm
FACILITATOR:- UDAY SAAN
START MONTH;- NOV-18-1W
END MONTH:- JAN-19 4W
NO OF PROJECTS COMPLETED:-1
MEMBERS
1.SAJIN
2. BHASKAR
3. SHIV KUMAR
4. VIGNESH
5. ARUN
SL NO | ITEM | PDCA | RESP | PLAN / ACTUAL | N0V-18 |  |  |  | DEC-18 |  |  |  | JAN-19 |  |  | 
 |  |  |  |  | 1W | 2W | 3W | 4W | 1W | 2W | 3W | 4W | 1W | 2W | 3W | 4W
1 | SELECTION OF THE THEME | PLAN | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
2 | GRASP THE CURRENT SITUATION & SETTING THE GOAL | PLAN | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
3 | DRAWING THE ACTION | PLAN | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
4 | ANALYSIS OF THE RELAVENT FACTORS | DO | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
5 | EXAMINATION & IMPLEMENTATION OF COUNTERMEASURES | DO | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
6 | CONFIRMATION OF THE EFFECTS | CHECK | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
7 | STANDARDIZATION | ACT | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
Notes: SAJIN: THIS IS OUR ACTIVITY PLAN.

## Slide 7
THEME SELECTION
Notes: SAJIN: LETS IDENTIFY THE AREAS FOR IMPROVEMENTS.

## Slide 8
SELECTION OF THE THEME
PRODUCTIVITY IMPROVEMENT
5S IMPROVEMENT
REWORK REDUCTION
OEE IMPROVEMENT
REJECTION REDUCTION
CAPACITY IMPROVEMENT
Notes: SAJIN :LETS EVALUATE THE PROBLEM BY KJ METHOD

## Slide 9
 | SERIOUSNESS OF THE NEED FOR AN IMPROVEMENT |  |  | CIRCLE CAPABILITY |  |  | APPLICATION OF QC TOOLS | TOTAL EVALUATION POINTS | GRAPH OF EVALUATION POINTS |  |  |  |  | 
 | DEGREE OF IMPORTANCE | URGENCY | ECONOMC FACTOR | CAN EVERY ONE PARTICIPATE | CAN CIRCLE SOLVE PROBLEM BY THEMSELVES | CAN FINISH WITH IN THE TARGET TIME |  |  |  |  |  |  |  | 
QUALITY |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PRODUCTIVITY | ◎ |  |  |  | ◎ | ◎ | ◎ |  |  |  |  |  |  | 
COST |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DELIVERY | ◎ | ◎ |  |  |  |  |  |  |  |  |  |  |  | 
EVALUATION CRITERIA
◎
5 POINTS
3 POINTS
1 POINT
PROBLEM EVALUATION BY KJ METHOD
PROBLEM POINT
EVALUATION BY KJ METHOD
33
31
21
23
◎
◎
◎
◎
◎
◎
◎
◎
◎
Notes: REWORK HAS GOT MAXIMUM POINTS SO WE SELECT REWORK FOR IMPROVEMENTS

## Slide 10
WHAT ARE THE QUALITY PROBLEMS
REJECTION
REWORK
FITTMENT ISSUE
SINCE REJECTION IS HIGH CONSIDERD, REJECTION ANALYSIS ON PRIORITY.
MODEL MIXUP
DELIVERY DELAY
SAFETY ISSUE

## Slide 11
TYPES OF DEFECTS LEADS TO REJECTION
ID OVER SIZE
RUST PARTS
SPLINE DENT
OBD U/S
CUTTER MARK
FACE UNCLEAR
TCE
FACE R/O
PCD R/O
TEETH DENT & DAMAGE
SPLINE DAMAGE
ID O/S & OD U/S
Notes: SAJIN : WHAT ARE THE MAJOR REWORK IN THE LINE

## Slide 12
THE CONTRIBUTION Of GEAR COUNTER = 28.9%
REJECTION DETAILS GEAR A SECTION
REJECTION DETAILS OF THE GEAR A SECTION |  |  |  |  |  |  |  | 
COMPONENT | UOM | Jun-18 | Jul-18 | Aug-18 | Sep-18 | Oct-18 | Nov-18 | AVG QTY & %
GEAR COUNTER | QTY | 732 | 779 | 930 | 189 | 618 | 650 | 650
 | % | 0.49% | 0.45% | 0.60% | 0.13% | 0.45% | 0.59% | 0.45%
GEAR C2 -K 55 | QTY | 22 | 56 | 13 | 7 | 23 | 3 | 21
 | % | 0.29% | 0.21% | 0.23% | 0.27% | 0.23% | 0.44% | 0.28%
GEAR -C4 -K 55 | QTY | 141 | 65 | 66 | 112 | 83 | 76 | 91
 | % | 0.29% | 0.24% | 0.24% | 0.19% | 0.30% | 0.34% | 0.27%
GEAR FINAL KWP | QTY | 625 | 390 | 334 | 295 | 342 | 338 | 387
 | % | 0.32% | 0.14% | 0.13% | 0.28% | 0.23% | 0.39% | 0.25%
GEAR - M3 K55 | QTY | 116 | 98 | 136 | 81 | 126 | 63 | 103
 | % | 0.37% | 0.22% | 0.19% | 0.19% | 0.22% | 0.24% | 0.24%
GEAR PKS -K 55 | QTY | 135 | 79 | 109 | 128 | 89 | 62 | 100
 | % | 0.09% | 0.22% | 0.05% | 0.02% | 0.10% | 0.02% | 0.09%
Chart: PART WISE % CONTRIBUTION TO TOTAL REJECTION
| GEAR COUNTER | GEAR C2 -K 55 | GEAR -C4 -K 55 | GEAR FINAL KWP | GEAR - M3 K55 | GEAR PKS -K 55
 | 0.28863 | 0.17779 | 0.16919 | 0.15781 | 0.1521 | 0.054489
Notes: BHASKAR : HERE IS THE PART WISE REJECTION DETAILS IN GEAR A SECTION .
THE CONTRIBUTION OF GEAR COUNTER IS 28.9 %
SAJIN : WHAT ARE THE MAJOR DEFECTS IN THE GEAR COUNTER

## Slide 13
SECTION WISE REJECTION DETAILS
REJECTION IN GEAR A IS
0.60%
LETS FOCUS ON THE GEAR A FOR REJECTION REDUCTION
Chart: SECTION WISE REJECTION DETAILS FROM JUNE-18 TO NOV-18
| 43252 | 43282 | 43313 | 43344 | 43374 | 43405
GEAR A | 0.55 | 1.3 | 0.48 | 0.28 | 0.42 | 0.57
SHAFT | 0.67 | 0.68 | 0.56 | 0.37 | 0.39 | 0.35
CAM SHAFT | 0.46 | 0.38 | 0.39 | 0.29 | 0.29 | 0.49
GEAR B | 0.44 | 0.12 | 0.24 | 0.25 | 0.25 | 0.35
HARD | 0.35 | 0.36 | 0.17 | 0.15 | 0.17 | 0.18
CON ROD | 0.05 | 0.37 | 0.1 | 0.03 | 0.05 | 0.08
FORGING | 0.01 | 0.02 | 0.04 | 0.05 | 0.035 | 0.05
HONNING | 0.03 | 0.01 | 0.01 | 0.01 | 0.009 | 0.02
Chart: AVERAGE REJECTION
| GEAR A | SHAFT | CAM SHAFT | GEAR B | HARD | CON ROD | FORGING | HONNING
TOTAL REJECTION | 0.006 | 0.0050333 | 0.0038333 | 0.00275 | 0.0023 | 0.0011333 | 0.00034167 | 0.00014833
Notes: SAJIN : WHAT ARE THE MAJOR REWORK IN THE LINE

## Slide 14
THE CONTRIBUTION Of GEAR COUNTER = 31%
REJECTION DETAILS GEAR A SECTION
TOTAL REJECTION IN THE GEAR A SECTION PART WISE |  |  |  |  |  |  | 
COMPONENT | Jun-18 | Jul-18 | Aug-18 | Sep-18 | Oct-18 | Nov-18 | TOTAL
GEAR COUNTER | 732 | 779 | 930 | 189 | 618 | 650 | 3898
GEAR FINAL | 625 | 390 | 334 | 295 | 342 | 338 | 2324
GPDN -TVS STAR | 997 | 171 | 119 | 50 | 176 | 330 | 1843
GEAR INTERMEDIATE-WEGO | 374 | 714 | 419 | 182 | 382 | 296 | 2367
GPDN -K14F | 83 | 102 | 96 | 138 | 86 | 133 | 638
GEAR REAR WHEEL-WEGO | 49 | 300 | 76 | 107 | 48 | 78 | 658
GPDN -TVS APACHE | 408 | 125 | 172 | 170 | 72 | 33 | 980
Chart: TOTAL REJECTION FROM JUNE 18 TO NOV 18
| GEAR COUNTER | GEAR FINAL | GPDN -TVS STAR | GEAR INTERMEDIATE-WEGO | GPDN -K14F | GEAR REAR WHEEL-WEGO | GPDN -TVS APACHE
 | 3898 | 2324 | 1843 | 2367 | 638 | 658 | 980
Notes: PRAMOD: THE MAJOR REWORK WERE FORK TIGHT, OD DENT, BORE U/S & GEAR TEETH DENT. OUT OF WHICH FORK TIGHT IS CONTRIBUTING 48%.
SAJIN: IN WHICH PART FORK TIGHT IS COMIN MORE?
MANOHAR: THE MAJOR PARTS CONTRIBUTING TO FORK TIGHT IS M3,C4,C3,M4 . IN THIS GEAR M3 IS CONTRIBUTING MORE WHICH IS 67%.
SAJIN: LETS SELECT M-3 FOR THE IMPROVEMENTS

## Slide 15
THE MAJOR REJECTION IN GEAR COUNTER IS TCE OUT
THE AVREAGE REJECTION PERCENTAGE = 0.29%
REJECTION DETAILS
GEAR COUNTER | Jun-18 | Jul-18 | Aug-18 | Sep-18 | Oct-18 | Nov-18 | TOTAL
TCE OUT | 238 | 439 | 595 | 105 | 153 | 397 | 1927
TEETH DAMAGE | 272 | 176 | 170 | 46 | 113 | 96 | 873
BROACHING SPLINE DAMAGE | 93 | 73 | 31 | 5 | 45 | 17 | 264
OBD U/S |  | 28 | 6 | 1 | 225 |  | 260
ID O/S | 48 | 13 | 31 | 3 | 19 | 62 | 176
DENT & DAMAGE | 22 | 21 | 21 | 5 | 48 | 12 | 129
OD U/S | 17 | 10 | 14 | 3 |  | 46 | 90
Chart: TCE MORE DETAILS FROM JUNE 18 TO NOV -18
| 43252 | 43282 | 43313 | 43344 | 43374 | 43405
TCE OUT | 238 | 439 | 595 | 105 | 153 | 397
TEETH DAMAGE | 272 | 176 | 170 | 46 | 113 | 96
BROACHING SPLINE DAMAGE | 93 | 73 | 31 | 5 | 45 | 17
OBD U/S | 28 | 6 | 1 | 225
ID O/S | 48 | 13 | 31 | 3 | 19 | 62
DENT & DAMAGE | 22 | 21 | 21 | 5 | 48 | 12
OD U/S | 17 | 10 | 14 | 3 | 46
Chart: TCE REJECTION % WISE
| 43252 | 43282 | 43313 | 43344 | 43374 | 43405
 | 0.0015292 | 0.002857 | 0.0037059 | 0.0025 | 0.0029 | 0.0036249
Notes: BHASKAR : HERE IS THE LAST SIX MONTHS DEFECT WISE REJECTION DETAILS OF GEAR COUNTER
TCE MORE IS THE MAJOR DEFECT
YOU CAN SEE THAT THE REJECTION HAS INCREASED FROM

## Slide 16
GEAR COUNTER TCE OUT REJECTION REDUCTION
THEME
THEME
REDUCING TCE OUT FROM 0.29% TO O.O32%
TARGET
Notes: SAJIN: OUR THEME IS & OUR TARGET IS
PRAVEEN: THEME & TARGET ( ALL MEMBER SAY ZERO)

## Slide 17
Definition
of the Problem

## Slide 18
HOW TO CHECK IS TCE
THE DIFFERENCE OF MIN TO MAX ERROR IN ONE ROTATATION OF GEAR
IDEAL CONDITION
MASTER GEAR
GEAR
DIAL
Notes: SHIVKUMAR : WHAT IS TCE
SAJIN : EXPLAIN THE TCE
HAVE YOU ANALYSED THE REJECTION PART IN DETAILS

## Slide 19
WHAT IS TCE (TOTAL COMPOSITE ERROR)
THE DIFFERENCE OF MIN TO MAX ERROR IN ONE ROTATATION OF GEAR
Notes: SHIVKUMAR : WHAT IS TCE
SAJIN : EXPLAIN THE TCE
HAVE YOU ANALYSED THE REJECTION PART IN DETAILS

## Slide 20
DEFECT PARTS INVESTIGATION
PART | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
TCE | 0.080 | 0.090 | 0.085 | 0.080 | 0.090 | 0.100 | 0.070 | 0.075 | 0.080 | 0.090
PCD | 0.080 | 0.090 | 0.070 | 0.090 | 0.085 | 0.085 | 0.060 | 0.070 | 0.075 | 0.080
PARALLALISM | 0.070 | 0.075 | 0.080 | 0.080 | 0.075 | 0.070 | 0.065 | 0.080 | 0.060 | 0.070
FACE R / O | 0.060 | 0.072 | 0.086 | 0.072 | 0.068 | 0.080 | 0.062 | 0.073 | 0.065 | 0.062
STRONG CO-RELATION EXISTS FOR TCE IN RELATION TO PCD , PARALLILISM & FACE R/O
Chart: TCE
TCE TARGET | 0.045 | 0.045 | 0.045 | 0.045 | 0.045 | 0.045 | 0.045 | 0.045 | 0.045 | 0.045
TCE ACTUAL | 0.08 | 0.09 | 0.085 | 0.08 | 0.09 | 0.1 | 0.07 | 0.075 | 0.08 | 0.09
Chart: PCD
PCD TARGET | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03
PCD ACTUAL | 0.08 | 0.1 | 0.07 | 0.09 | 0.085 | 0.085 | 0.06 | 0.07 | 0.075 | 0.08
Chart: PARALLELISM
PARALLALISM TARGET | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02
PARALILISM ACTUAL | 0.07 | 0.075 | 0.08 | 0.08 | 0.075 | 0.07 | 0.065 | 0.08 | 0.06 | 0.07
Chart: FACE R/O
FACE R/O TARGET | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03
FACE R/O ACTUAL | 0.06 | 0.072 | 0.086 | 0.072 | 0.068 | 0.08 | 0.062 | 0.073 | 0.065 | 0.062
Notes: BHASKAR : I HAVE ANALYSED THE REJECTION PART.
TAKEN 10 TCE OUT PARTS AND CHECKED ALL THE PARAMETERS
BHASKAR : CO RELATED THE PARAMETERS WITH THE TCE

## Slide 21
PROCESS FLOW OF GEAR COUNTER
FORGING
TURNING-1
TURNING-2
BROACHING
HOBBING
HEAT
TREATMENT
INSPECTION
ASSEMBLY
HMSI -NARASAPURA
SHAVING
Notes: MANOHAR: our manufacturing process start from. Forging
PRAMOD: turning-1
PRAVEEN: turning-2
MANOHAR: broaching
PRAMOD: shaping
PRAVEEN: heat treatment
MANOHAR: inspection
PRAMOD: assy
PRAVEEN: OUR BUSSINESS PARTNER IS HONDA
SAJIN: WHERE FORK TIGHT IS GENERATING?
PRAVEEN: TURNING-2
SAJIN: DID WE HAVE THE REWORK DATA?

## Slide 22
LETS FOCUS ON TURNING

## Slide 23
HARDNESS VARIATION
INPUT STOCK VARIATION
UN SKILLED ASSOCIATE
INSERT
CHUCK R/O SETTING
WEAR PART CONDITION
PART HOLDING DEVICES
SEAT CHECK
COOLANT PIPE POSITION
TCE OUT
SAKANA NO HONE (FISH BONE)
NG PART HANDLING
CUTTING PARAMETERS
TOOL PATH
INSERT WEAR
GAUGING
COOLENT PIPE POSITION
CUTTER R/O
PART MASTER R/O
FIXTURE R/O
VERTICAL TOOL ALIGNMENT
MACHINE BED PARALLISM
TOOL CLAMPING
VERTICAL TOOL ALIGNMENT
HOB ARBOUR R/O
TAILSTOCK R/O
CUTTER FACE R/O
CHIP EVACUATION
VARIATION AFTER SHAVING
ID UNDERSIZE
WORK ARBOR DIA
Notes: SAJIN: THE MAJOR FACTORS RELATED TO MACHINE
MANOHAR: 2 points read
SAJIN: man
PRAMOD: read points
SAJIN: method
PRAVEEN: read all points
SAJIN: there is no cause in material
PRAVEEN: there is no causes in material found
SAJIN: lets du the factor analysis on these problem points

## Slide 24
PROBLEM ANALYSIS
Chart: PARALLELISM DATA AFTER TURNING
ACTUAL | 0.03 | 0.018 | 0.016 | 0.01 | 0.028 | 0.018 | 0.026 | 0.015 | 0.024 | 0.034 | 0.038 | 0.019 | 0.024 | 0.018 | 0.025 | 0.014 | 0.035 | 0.02 | 0.018 | 0.038 | 0.024 | 0.03 | 0.014 | 0.028 | 0.027 | 0.018 | 0.022 | 0.019 | 0.027 | 0.034
TARGET | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02
HERE 43% OF PARTS ARE OUT OF THE SPEC. AND Cpk NOT ACHIEVED.
LETS DO THE SAKANA NO HONE ANALYSIS.
SAMPLE TAKEN FROM MASS PRODUCTION PARTS
Cp = 0.39
Cpk =-0.15
PROCESS CAPABILITY OF PARALLELISM
Notes: SAJIN: WHAT IS TCE
BHASKAR : TCE IS MEASURED BY USING GRT
IT IS THE

## Slide 25
ONLY THE PUSHER LUG EDGE IS PUSHING THE PART
GEMBA VERIFICATION
PUSHER PLATE IS NOT PUSHING THE PART PROPERLY
PUSHER IS CLAMPING THE PART IN THE GROOVE
PUSHER DESIGN IS NG
LETS MODIFY THE PUSHER DESIGN
HERE IS HOW THE MODIFIED PUSHER PUSH THE PART
Chart: PARALLISM IN TURNING
BEFORE | 0.03 | 0.018 | 0.016 | 0.01 | 0.028 | 0.018 | 0.026 | 0.015 | 0.024 | 0.034 | 0.038 | 0.019 | 0.024 | 0.018 | 0.025 | 0.014 | 0.035 | 0.02 | 0.018 | 0.038 | 0.024 | 0.03 | 0.014 | 0.028 | 0.027 | 0.018 | 0.022 | 0.019 | 0.027 | 0.034
SPEC | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02
AFTER | 0.015 | 0.016 | 0.016 | 0.014 | 0.012 | 0.012 | 0.01 | 0.013 | 0.014 | 0.01 | 0.013 | 0.012 | 0.012 | 0.01 | 0.012 | 0.01 | 0.013 | 0.012 | 0.013 | 0.012 | 0.01 | 0.011 | 0.012 | 0.01 | 0.01 | 0.013 | 0.012 | 0.01 | 0.01 | 0.01
PROCESS CAPABILITY OF PARALLELISM
Cp =2.54
Cpk =2.04

## Slide 26
LETS FOCUS ON BROACHING

## Slide 27
PROBLEM ANALYSIS
Chart: FACE RUNOUT AFTER BROACHING
ACTUAL | 0.05 | 0.028 | 0.03 | 0.022 | 0.044 | 0.034 | 0.04 | 0.03 | 0.038 | 0.056 | 0.052 | 0.03 | 0.044 | 0.03 | 0.046 | 0.03 | 0.05 | 0.032 | 0.034 | 0.084 | 0.044 | 0.058 | 0.03 | 0.056 | 0.058 | 0.038 | 0.04 | 0.038 | 0.045 | 0.05
TARGET | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03
HERE 70% OF PARTS ARE OUT OF THE SPEC & Cpk NOT ACHIEVED
LET’S DO THE SAKANA NO HONE ANALYSIS.
SAMPLE AFTER PARALLELISM CORRETION
Cp = 0.38
Cpk = -0.31
Notes: SAJIN: WHAT IS TCE
BHASKAR : TCE IS MEASURED BY USING GRT
IT IS THE

## Slide 28
SI NO | FACTOR | CONFIRMATION POINTS | INSPECTION CRITERIA | OBSERVATION / IMPROVEMENT POINTS | JUDGE
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  | TOOL ALIGNMENT SHOULD BE WITH IN 0.010 MM |  | 
6 | MACHINE | BED PARALLELISM | PARALLELISM TO BE WITH IN 0.010 MM |  | 
FACTOR ANALYSIS
MATERIAL
HARDNESS VARIATION
HARDNESS SPEC
80 ~ 95 HRB
HARDNESS IS WITH IN SPEC
METHOD
TOOL WEAR
CHECKED FOR THE TOOL WEAR
METHOD
CUTTING PARAMETERS
CHECK PARAMETERS IN PROGRAM
MAN
COOLANT PIPE POSITION
VERIFIED THE COOLENT FLOW AT CUTTING AREA
MACHINE
VERTICAL TOOL ALIGNMENT
Chart: GEAR COUNTER SOZAI HARDNESS
ACTUAL | 85.8 | 86.1 | 86.4 | 86.9 | 86.8 | 87.6 | 85.9 | 87 | 87 | 86.8 | 86.4 | 86.2 | 86.7 | 86.3 | 85 | 85.7 | 85.6 | 86.3 | 86.2 | 85.1 | 85.5 | 85.8 | 85.6 | 86.1 | 86.2 | 85.9 | 86.7 | 85.7 | 85.8 | 86.2
MIN | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80
MAX | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95
Notes: MANOHAR: Machine: 2 points( all together say….. Ok (loudly with thump show) after saying judgment is……….
PRAVEEN: NEXT VARIATION AFTER SHAPING

## Slide 29
SI NO | FACTOR | CONFIRMATION POINTS | INSPECTION CRITERIA | OBSERVATION / IMPROVEMENT POINTS | JUDGE
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  | TOOL ALIGNMENT SHOULD BE WITH IN 0.010 MM |  | 
6 | MACHINE | BED PARALLELISM | PARALLELISM TO BE WITH IN 0.010 MM |  | 
FACTOR ANALYSIS
MATERIAL
HARDNESS VARIATION
HARDNESS SPEC
80 ~ 95 HRB
HARDNESS IS WITH IN SPEC
METHOD
TOOL WEAR
CHECKED FOR THE TOOL WEAR
NO WEAR FOUND IN THE TOOL
METHOD
CUTTING PARAMETERS
CHECK PARAMETERS IN PROGRAM
ALL PARAMETERS WERE AS PER LOGIC
MAN
COOLANT PIPE POSITION
VERIFIED THE COOLENT FLOW AT CUTTING AREA
COOLANT FLOW NOT OK
MACHINE
VERTICAL TOOL ALIGNMENT
ALIGNMENT FOUND 0.10 MM AND PULL END LOCK FOUND NG
PARALLISM FOUND 0.080
Notes: MANOHAR: Machine: 2 points( all together say….. Ok (loudly with thump show) after saying judgment is……….
PRAVEEN: NEXT VARIATION AFTER SHAPING

## Slide 30
GEMBA VERIFICATION
IDEALLY - THE FLUSHING SHOULD BE ON THE WORK REST TO AVOID CHIP ACCUMULATION
THE FLUSHING PIPES GETTING DISTURBED DURING CONTINIOUS OPERATION
WHAT TO BE DONE
NEED TO PREVENT THE MOVEMENT OF FLUSHING PIPE
LETS GO FOR PERMANENT ACTION
FLEXIBLE PIPES REPLACED WITH METAL PIPES
FIXED METAL PIPES

## Slide 31
LETS FOCUS ON
HOBBING

## Slide 32
SI NO | FACTOR | CONFIRMATION POINTS | INSPECTION CRITERIA | OBSERVATION / IMPROVEMENT POINTS | JUDGE
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
5 |  |  | ARBOR DIA SPEC 13.504 ~13.517 MM |  | 
6 | METHOD | CHIP EVACUATION | NO CHIP ALLOWED IN PART RESTING AREA |  | 
FACTOR ANALYSIS
MACHINE
HOB ARBOUR RUNOUT
RUNOUT WITH IN 0.010 MM
FOUND 0.008MM
MACHINE
TAILSTOCK RUNOUT
RUNOUT WITH IN 0.010 MM
FOUND 0.010 MM
METHOD
CUTTING PARAMETERS
CHECK PARAMETERS IN PROGRAM
ALL PARAMETERS WERE AS PER LOGIC
MAN
CUTTER RUNOUT
RUNOUT WITH IN 0.010 MM
FOUND 0.008MM
MATERIAL
WORK ARBOUR DIA
ARBOR DIA FOUND 13.454 MM
CHIPS ACCUMILATED IN PART RESTING AREA
Notes: MANOHAR: Machine: 2 points( all together say….. Ok (loudly with thump show) after saying judgment is……….
PRAVEEN: NEXT VARIATION AFTER SHAPING

## Slide 33
CHIPS IN FIXTURE
AIR FLUSHING POINTS
AIR FLUSHING POINTS
CHIPS ACCUMILATION ELIMINATED
CHIP AT CLAMPING
TOP CLAMP
RESTING FIXTURE
COMPONENT
CHIPS IN FIXTURE
Cp = 4.30
Cpk = 1.63
Chart: PCD R/O AFTER KAIZEN
BEFORE | 0.042 | 0.014 | 0.025 | 0.018 | 0.034 | 0.025 | 0.028 | 0.022 | 0.025 | 0.04 | 0.038 | 0.025 | 0.022 | 0.018 | 0.028 | 0.014 | 0.042 | 0.018 | 0.014 | 0.064 | 0.0025 | 0.045 | 0.016 | 0.025 | 0.028 | 0.018 | 0.014 | 0.016 | 0.025 | 0.032
TARGET | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03
AFTER | 0.024 | 0.022 | 0.026 | 0.024 | 0.024 | 0.026 | 0.024 | 0.025 | 0.027 | 0.025 | 0.025 | 0.025 | 0.024 | 0.025 | 0.025 | 0.022 | 0.024 | 0.024 | 0.024 | 0.024 | 0.024 | 0.025 | 0.024 | 0.025 | 0.022 | 0.024 | 0.024 | 0.022 | 0.025 | 0.026

## Slide 34
Chart: GEAR COUNTER TCE REJECTION
| Nov-18 | DEC-W1 | DEC-W2 | DEC-W3 | JAN-W1 | JAN-W2 | JAN-W3 | JAN-W4
 | 397 | 18 | 16 | 13 | 12 | 10 | 7 | 6
EFFECT CONFIRMATION
PARALLILISM OUT ELIMINATION
FACE RUN OUT CORRECTION
PCD R/O ELIMINATION IN HOBBING
2
3
AFTER IMPLIMENTATION ALL THE KAIZENS TCE REJECTION REDUCEED .
1
(47 NOS – 0.06%
(35 NOS – 0.03%

## Slide 35
ACTIVITY SCHEDULE PLANNING
CIRCLE NAME: HORIZON
PROJECT:- TCE REDUCTION
Meeting time every Friday 3 to 4 pm
FACILITATOR:- UDAY SAAN
START MONTH;- NOV-18-1W
END MONTH:- JAN-19 4W
NO OF PROJECTS COMPLETED:-1
MEMBERS
1.SAJIN
2. BHASKAR
3. SHIV KUMAR
4. VIGNESH
5. ARUN
SL NO | ITEM | PDCA | RESP | PLAN / ACTUAL | N0V-18 |  |  |  | DEC-18 |  |  |  | JAN-19 |  |  | 
 |  |  |  |  | 1W | 2W | 3W | 4W | 1W | 2W | 3W | 4W | 1W | 2W | 3W | 4W
1 | SELECTION OF THE THEME | PLAN | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
2 | GRASP THE CURRENT SITUATION & SETTING THE GOAL | PLAN | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
3 | DRAWING THE ACTION | PLAN | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
4 | ANALYSIS OF THE RELAVENT FACTORS | DO | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
5 | EXAMINATION & IMPLEMENTATION OF COUNTERMEASURES | DO | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
6 | CONFIRMATION OF THE EFFECTS | CHECK | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
7 | STANDARDIZATION | ACT | TEAM | PLAN |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  |  | 
Notes: PRAVEEN: THIS IS OUR ACTIVITY PLAN.

## Slide 36
SUMMARY
AFTER THE KAIZENS & CORRECTIVE ACTIONS
THE RESULTS
THE TCE REJECTION HAS BEEN REDUCEED
Chart: REJECTION COST MONTH WISE
| 43405 | 43435 | 43466
 | 31402 | 3717 | 2768
Chart: TCE REJECTION QTY & % WISE
| 43405 | 43435 | 43466
REJ. QTY | 397 | 47 | 35
% REJECTION | 0.0035973 | 0.00059996 | 0.00030247
TOTAL SAVING :
0.343 MIL / ANNUM

## Slide 37
Brain storming
Cause and Effect Diagram
We used following QC tools & Techniques for our project
KJ METHOD
QC TOOLS & TECHNICS USED
Histogram
Graph
Notes: MANOHAR

## Slide 38
PARAMETER | BENIFITS | REMARK
PRODUCTION | PRODUCTIVITY IMPROVED | 
QUALITY | REJECTION REDUCED | 
COST | COST OF QUALITY REDUCED | 
DELIVERY | ON TIME DELIVERY | 
SAFTEY | ZERO ACCIDENT | 
MORAL | OPERATOR FATIGUE REDUCED | 
IN TANGEBLE BENIFITS

## Slide 39
THANK YOU
Notes: BE TOGETHER