## Slide 1
MUSASHI AUTO PARTS INDIA PVT LIMITED
BANGALORE PLANT
No Limitations For Improvements……….
WELCOMES
YOU ALL to NHC-2018
HORIZON

## Slide 2
HARYANA
INDIA
BANGALORE
BAWAL
KARNATAKA
BANGALORE
BAWAL
LOCATIONS of map-id

## Slide 3
OUR MAJOR CUSTOMERS ARE HONDA, EXEDY AND TVS.
WE MANUFACTURING :
TRANSMISSION SHAFT,
TRANSMISSION GEAR,
CON ROD & CAM SHAFT
ABOUT OUR PLANT

## Slide 4
TEAM INRTRODUCTION
LEADER
ADVISOR
KOHJI SAN
STRENGTH: GIVING IDEAS
PRAVEEN SAN
STRENGTH: PROGRAMMING
MANOHAR SAN
STRENGTH: PART SETTING
PRAMOD SAJN
STRENGTH: TOOLING
BHASKAR SAN
STRENGTH: INFORMATION TOWER
SAJIN
STRENGTH: MACHINING

## Slide 5
Selection of the CIRCLE THEME

## Slide 6
Selection of the theme
 | SERIOUSNESS OF THE NEED FOR AN IMPROVEMENT |  |  | CIRCLE CAPABABILITY |  |  | APPLICATION OF QC TOOLS | TOTAL EVALUATION POINTS | GRAPH OF EVALUATION POINTS |  |  |  |  | 
 | DEGREE OF IMPORTANCE | URGENCY | ECONOMC FACTOR | CAN EVERY ONE PARTICIPATE | CAN CIRCLE SOLVE PROBLEM BY THEMSELVES | CAN FINISH WITH IN THE TARGET TIME |  |  |  |  |  |  |  | 
REWORK | ◎ |  |  | ◎ | ◎ | ◎ | ◎ | 31 |  |  |  |  |  | 
REJECTION | ◎ | ◎ |  |  | ◎ | ◎ |  | 27 |  |  |  |  |  | 
PRODUCTIVITY | ◎ | ◎ |  |  |  |  |  | 17 |  |  |  |  |  | 
EVALUATION CRITERIA
◎
5 POINTS
3 POINTS
1 POINT
BASED ON THE ABOVE EVALUATION THEME “REWORK ELIMINATION” IS SELECTED.

## Slide 7
Chart: GEAR KTEL REWORK QUANTITY COMPONENT WISE JULY -17 TO SEP-17
| M3 | C4 | M4 | PKS | GPD | M2 | GKIS | GSDN | C2 | C3 | C1
 | 3118 | 1025 | 510 | 180 | 130 | 126 | 110 | 104 | 104 | 94 | 70
 | 0.55968 | 0.74367 | 0.83522 | 0.86753 | 0.89086 | 0.91348 | 0.93323 | 0.95189 | 0.97056 | 0.98743 | 1
PARETO ANALYSIS OF THE REWORK DONE FOR FORK TIGHT
83.52% PROBLEM FOUND IN THE 1st 3 COMPONENTS, OUT OF THIS M3 IS HAVING THE
HEIGHTEST REWORK QUANTITY. SO WE SELECTED M-3 TO DO THE IMPROVEMENT
REWORK STATUS PARTS WISE

## Slide 8
Chart: GEAR M-3 FORK TIGHT REWORK STATUS
| FORK TIGHT | SPLINE DENT | SPLINE TIGHT | BURR
 | 2674 | 236 | 123 | 85
WE HAVE COLLECTED THE DATA FOR REWORK IN GEAR M3 & FOUND THE ABOVE REASONS FOR THE REWORK .
THE MAJOR REWORK IS DONE DUE TO FORK TIGHT WITH 10% REJ. APPROX.
REWORK STATUS PROBLEM WISE

## Slide 9
ACHIEVING A REDUCTION IN THE FORK TIGHT DEFECT IN ASSEMBLY
REDUCING THE FORK TIGHT PART MOVING TO ASSEMBLY TO ZERO.
THEME
TARGET
theme
Chart: AVG. M3 FORK TIGHT REWORK TIME / MONTH
| CURRENT | TARGET
 | 267 | 0
Chart: AVG M3 COMPONENT REWORK / MONTH
| CURRENT | TARGET
 | 535 | 0

## Slide 10
ACTIVITY START BY OCT-2017 AND END BY NOV-2017. .
REWORK ELIMINATION ACTIVITY PLANNING
MIQC NAME: THE TEAM HORIZON
PROJECT;- FORK TIGHT REWORK ELIMINATION
Meeting time every Friday 3 to 4 pm
FACILITATER;- KOHJI SAN
START MONTH;- OCT-17
END MONTH;- NOV-17
NO OF PROJECTS COMPLETED;-1
MEMBERS
1.SAJIN SAN
2.PRAVEEN SAN
3.MANOHAR SAN
4. PRAMOD SAN
5. BHASKAR SAN

## Slide 11
fork in the Motorcycle
WHAT IS THE FORK AND HOW IT WORKS
THE FORK IS USED FOR SHIFTING THE GEARS IN MOTORCYCLE.

## Slide 12
Analysis of the Problem

## Slide 13
DEFINITION OF THE PROBLEM
WHAT IS FORK TIGHT ?
HOW FORK TIGHT OCCURS ?
WHAT PROBLEM OCCURS IF FORK TIGHT MOVE TO CUSTOMER ?
GROOVE WIDTH
IF THE GROOVE WIDTH BECOME UNDER SIZE THAN SPECIFICATION.
IF THE MATERIAL LEFT IN THE CORNERS OF THE GROOVE
IF THE SURFACE ROUGHNESS ON THE GROOVE FACE OUT OF SPEC
CUSTOMER WILL LOOSE TRUST ON US
ASSEMBLY WILL NOT BE POSSIBLE
CUSTOMER LINE STOP
OK
NG
THE CONDITION IN WHICH THE FORK WILL NOT ENTER IN TO THE GROOVE OF COMPONENT

## Slide 14
PROCESS FLOW CHART OF gear m3
Out Sourcing
(SCr420HV 2(ID))
10
20
30
40
50
C01
60
70
80
90
100
110
C02
C03
120
C04
130
C05
PARTS FOR ASSEMBLY
140

## Slide 15
DATA SHOWING THE FORK TIGHT REWORK
AN AVERAGE OF 500 COMPONENTS WERE REWORKED IN EVERY MONTH
267 MINUTES (5HRS) BEING UTILIZED FOR THE REWORK EVERY MONTH
THIS IS AFFECTING THE OEE .
Chart: M-3 FORK TIGHT
BEFORE KAIZEN REWORK DATA
Chart: M-3 FORK TIGHT
| 42856 | 42887 | 42917 | 42948 | 42979
QTY | 475 | 467 | 576 | 524 | 632
TIME | 237.5 | 233.5 | 288 | 262 | 316

## Slide 16
CURRENT SITUATION ANALYSIS
CAUSE
TURNING
BROACHING
SHAPING
HT
PRIORITY
GROOVE WIDTH UNDER SIZE
GROOVE DIAMETER
OVER SIZE
TOOL WEAR
X
X
X
X
= 3
= 1
= 0
X
7
4
6
ANALYSIS DONE TO FIND OUT WHICH CAUSES CAN CONTRIBUTE TO THE FORK TIGHT.
X

## Slide 17
Inference; we identified 12 causes .
ANALYSIS DONE ON TURNING-2 TO FIND OUT THE VARIATION IN FORK WIDTH
ANALYSIS ON CURRENT SITUATION
Chart: FORK WIDTH
| 1 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240
ACTUAL | 5.18 | 5.175 | 5.175 | 5.185 | 5.18 | 5.17 | 5.175 | 5.17 | 5.165 | 5.175 | 5.17 | 5.155 | 5.135
UCL | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19
LCL | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15
Chart: FORK WIDTH
| 1 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240
ACTUAL | 5.17 | 5.17 | 5.175 | 5.18 | 5.18 | 5.17 | 5.165 | 5.17 | 5.17 | 5.155 | 5.16 | 5.15 | 5.14
UCL | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19
LCL | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15
Chart: FORK WIDTH
| 1 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240
ACTUAL | 5.175 | 5.185 | 5.175 | 5.175 | 5.18 | 5.18 | 5.165 | 5.17 | 5.165 | 5.175 | 5.145 | 5.135
UCL | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19
LCL | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15

## Slide 18
Fork tight
AXIS REPEATABILITY ERROR
OFFSET ERROR
INSERT LIFE LESS
Inference; we identified 12 causes .
TRAINEES
CUTTING PARAMETER
TOOL PATH
COOLANT CONDITION
INSERT NOT CHANGING AS PER FREQUENCY
INSERT TOLERANCE
HARDNESS VARIATION
DISTORTION NG
BRAIN STORMING WAS DONE TO FIND OUT WAYS TO ELIMINATE THE FORK TIGHT.
PART CLAMPING
TOOL LIFE LESS
TOOL HOLDING
COOLANT NOT COMING
UNSKILLED ASSOCIATE
IDEA GENERATION

## Slide 19
MAN
MACHINE
METHOD
MATERIAL
HARDNESS VARIATION
INPUT STOCK VARIATION
INSERT TOLERANCE
COOLANT CONDITION
CUTTING PARAMETER
TOOL PATH
UN SKILLED ASSOSICIATE
TRAINEES
INSERT NOT CHANGE AS PER FREQUENCY
OFFSET ERROR
TOOL LIFE
COOLENT NOT COMING
AXIS REPEATABILITY ERROR
PART CLAMPING
TOOL HOLDING
DISTORTION IN H/T
WHY FORK TIGHT HAPPENED
Sakana no hone (fish bone)
No. | SUSPECT
① | DISTORTION IN HT
② | TOOL LIFE
③ | TOOL PATH
④ | TOOL OFFSET
⑤ | INSERT TOLERENCE

## Slide 20
Trail Implementation and Checking Performance

## Slide 21
SUSPECT NO-1
No. | SUSPECT
① | DISTORTION IN HT
② | TOOL LIFE
③ | TOOL PATH
④ | TOOL OFFSET
⑤ | INSERT TOLERENCE

## Slide 22
Chart: HT DISTORTION STUDY - HARD STAGE
HARD ACTUAL | 5.13 | 5.14 | 5.15 | 5.14 | 5.14 | 5.14 | 5.14 | 5.15 | 5.14
HARD LCL | 5.11 | 5.11 | 5.11 | 5.11 | 5.11 | 5.11 | 5.11 | 5.11 | 5.11
HARD UCL | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15
ANY DISTORTION IS HAPPENING IN THE GROOVE WIDTH, IN HEAT TREATMENT ?
HOW CAN WE ENSURE THE SAME ?
IF WE CONDUCT THE 9 POINT STUDY ,WE CAN FIND THE DETAILS
HEAT TREATMENT DISTORTION STUDY
SOFT STAGE
5.1
HARD STAGE
Chart: HT DISTORTION STUDY - SOFT STAGE
SOFT ACTUAL | 5.17 | 5.17 | 5.18 | 5.17 | 5.16 | 5.17 | 5.16 | 5.17 | 5.17
SOFT LCL | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15 | 5.15
SOFT UCL | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19 | 5.19
STUDY RESULTS FOUND OK
NO PROBLEM FOUND IN HEAT TREATMENT
WHERE IS THE PROBLEM ?
+0.09
+0.05
5.1
+0.05
+0.01
Ave = 5.14
Ave = 5.17

## Slide 23
No. | SUSPECT
① | DISTORTION IN HT
② | TOOL LIFE
③ | TOOL PATH
④ | TOOL OFFSET
⑤ | INSERT TOLERENCE
SUSPECT NO-２

## Slide 24
WHY TOOL LIFE IS NOT ACHIEVING ?
TOOL LIFE IS NOT ACHIEVED AS PER THE SET LIFE DUE TO MATERIAL CHANGE FROM SCM TO SCR .
WHAT TO BE DONE ? LETS ANALYSIS IN DETAIL.
IS THE TOOL LIFE COMING AS PER THE STANDARD SET LIFE?
CURRENT CONDITION
LETS GO AND VERIFY AT GEMBA
CURRENT INSERT | A4G0405M04U04 GMN
SET LIFE | 500
ACTUAL LIFE | 200
CUTTING SPEED | 160
FEED | 0.2
MAKE | KENNAMETAL
BEFORE
AFTER
INSERT WEAR IS NOT GOOD
CHECKED IN GEMBA FOUND THAT LIFE NOT ACHIEVING AS PER STD

## Slide 25
INSERT WEAR IS NOT GOOD.
GROOVE OD BECOMING OVERSIZE (WITH BURR).
INSERT WEAR CHECK
PRESENT CONDITION
AFTER INSERT WEAR GROOVE WIDTH REDUCES & RADIUS FORMS IN THE CORNERS , AND ALSO FACE ROUGHNESS GETTING INCREASED
INSERT CORNERS IS CHIPPING OFF & RZ OUT OF SPEC. AFTER 200 NOS
GROOVE ROUGHNESS
Rz 17.37
RADIUS FORMED IN THE GROOVE CORNER
SPEC: ≤ 12.5
X

## Slide 26
Why-why ANALYSIS
INSERT GET CHIPPED OFF BEFORE REACHING SET LIFE
WHY
CUTTING PARAMETER IS NG
WHY
CUTTING PARAMETERS ARE NOT AS PER LOGIC
CUTTING PARAMETERS TO BE PUT AS PER LOGICAL CALCULATION
HOW
TOOL LIFE NOT ACHIEVING
WHY

## Slide 27
Chart: M-3 K67
| TURNING-1 | TURNING-2 | BROACHING | SHAPPING
AFTER | 27.18 | 26.81 | 17.38 | 22.64
CUTTING PARAMETER ARE NOT USED AS PER LOGICAL CALCULATION
CUTTING PARAMETER CHECK
LOGICAL CALCULATION AS F0LLOWS
G99G97S2000T303
G96 S160
G0 X46.35
G0 Z-21.15
G1 X22.8 F0.2
G0X35.0
G1 Z-20.03
G1 X22.8 F0.2
Rough theoretical value
Cutting speed
Rz max | ≤ 12.5
Cutting speed | Vc 100 ~ 140
Feed | F 0.12
TOOL PATH
M-3 cycle time
X

## Slide 28
Chart: TOOL LIFE
| TARGET | BEFORE | AFTER
 | 500 | 200 | 350
PARAMETERS CHANGED AS PER THE LOGICAL CALCULATION.
SURFACE ROUGHNESS ACHIEVED
WHY BURR NOT REMOVED & TOOL LIFE NOT ACHIEVED ? LETS CHECK FOR ALTERNATIVE GRADES
LOGICAL DATA IMPLEMENTATION
BEFORE
G99G97S2000T303
G96 S160
G00 X46.35
G00 Z-21.15
G01 X22.8 F0.2
G00X35.0
G01 Z-20.03
G01 X22.8 F0.2
G99G97S2000T303
G96 S120
G00 X46.35
G00 Z-21.15
G01 X22.8 F0.12
G00X35.0
G01 Z-20.03
G01 X22.8 F0.12
SETTING APPROVAL
MATERIAL LEFT-OFF NOT SOLVED
Rz : 4.18
AFTER
Chart: M-3 CYCLE TIME
| BEFORE | AFTER | AFTER IMPROVEMENT
 | 26.81 | 28.95 | 26.8
IMPROVEMENT IN TOOL PATH
SPEC: ≤ 12.5

## Slide 29
INSERT IS SELECTED BY CONSIDERING THE GEOMETRY , THE CHIP BREAKING ABILITY AND ADVICE FROM THE ADVISOR
INSERT SELECTION
CURRENT CHIP BREAKER
A4G0405M04U04 GMN
ALTERNATE CHIP BREAKERS
A4G0405M04U04 GUP
DTE400-040 -MOULDED
GY2M0400G040N-MM
DTE400-040 -GROUND
GDM4020N-040 GM

## Slide 30
 | BEFORE | AFTER
CURRENT INSERT | A4G0405M04U04 GMN | A4G0405M04U04 GUP
SET LIFE | 500 | 500
ACTUAL LIFE | 350 | 500
CUTTING SPEED | 120 | 120
FEED | 0.12 | 0.12
MAKE | KENNAMETAL | KENNAMETAL
TOOL LIFE IMPROVED .
WHY BURR COMING IN BETWEEN THE RUNS ?
IS THE TOOL PATH CORRECT ? . LETS CHECK THE SAME. .
NEW CHIP BREAKER TRIALS
AFTER
BEFORE
INSERT CORNER WEAR OUT AFTER 500 NOS
Chart: TOOL LIFE
| TARGET | ACTUAL
 | 500 | 500
Cp & Cpk
BURR IN GROOVE
CP1.42 & CPK1.37

## Slide 31
SUSPECT NO-３
No. | SUSPECT
① | DISTORTION IN HT
② | TOOL LIFE
③ | TOOL PATH
④ | TOOL OFFSET
⑤ | INSERT TOLERENCE

## Slide 32
Chart: FORK TIGHT
| SEP4W | Oct 1W | Oct 2W | Oct 3W
 | 116 | 564 | 102 | 154
TOOL PATH MODIFIED & OBSERVED FOR A WEEK .
FORK TIGHT COMPONANT AGAIN COMING
WHY FORK TIGHT COMING ? LETS ANALYSIS. .
TOOL PATH MODIFICATION
CHECKED THE TOOL PATH , CORRECTION NEEDS TO BE DONE
RETURN FINISHING CUTTING PATH
G00 Z-21.15
G01 X22.8 F0.12
G00X35.0
G01 Z-20.03
G01 X22.8 F0.12
G01Z-21.15
G01 X35.0F0.12
G00X50.0
G01 X22.8 F0.12
G00X35.0
G01 Z-20.03
G01 X22.8 F0.12
G01Z-21.15
G00X35.O W0.3F0.12
G01 Z-21.15
G01 X22.8 F0.12
FORWARD FINISHING CUTTING PATH
BEFORE CUTTING CONDITION
AFTER CUTTING CONDITION

## Slide 33
BUT FORK TIGHT ISSUE WAS NOT SOLVED
GROOVE WIDTH O/S PARTS FOUND
THEN WHO IS THE CULPRIT?
IS IT OFFSET ERROR?
IS IT THE INSERT TOLERENCE ?
LETS ANALYSE ONE BY ONE……………………….
TOOL LIFE ACHIEVED
DISTORTION OK
CP & CPK OK
REASONING

## Slide 34
SUSPECT NO-４
No. | SUSPECT
① | DISTORTION IN HT
② | TOOL LIFE
③ | TOOL PATH
④ | TOOL OFFSET
⑤ | INSERT TOLERENCE

## Slide 35
Chart: FORK TIGHT
| Oct 2W | Oct 3W | Oct 4W
 | 102 | 154 | 85
TOOL OFFSET CHANGED FROM `DOUBLE OFFSET TO SINGLE OFFSET.
PROGRAM CORRECTED
WHY STILL FORK TIGHT IS COMING. ? LETS CHECK OTHER SUSPECTS. .
TOOL OFFSET CHANGE
LETS ANALYSE THE CURRENT OFFSET CONDITION & WILL CORRECT THE ISSUE
2 OFFSET FOR GROOVE WIDTH CORRECTION
BEFORE
TO3
T13
G99G97S2000T303
G0X46.35
Z-21.15
G1X22.85F0.12
T13
G0X35.0
G1Z-20.11
G1X22.8F0.12
G99G97S2000T303
G0X46.35
Z-21.15
G1X22.85F0.12
GOX35.0
G1Z-20.03
G1X22.8
G04X05
AFTER
TOOL OFFSET WILL BE ONE OF THE REASON FOR GROOVE WIDTH O/S

## Slide 36
SUSPECT NO-５
No. | SUSPECT
① | DISTORTION IN HT
② | TOOL LIFE
③ | TOOL PATH
④ | TOOL OFFSET
⑤ | INSERT TOLERENCE

## Slide 37
TOOL LIFE ACHIEVED
DISTORTION OK
REASONING
OFFSET CORRECTED
THEN WHY IS THE FORK TIGHT COMING AGAIN ?
IS THERE ANY VARIATION IN INSERT TO INSERT ?
LETS CHECK THE SAME……………………….
CP & CPK OK

## Slide 38
THE MAX VARIATION COMING IS 0.143 MM
WHY VARIATION COMING IN DIFFERENT BATCHES ?. .
INSERT ANALYSIS
LETS PRODUCE THE PARTS ACCORDING TO BATCHWISE INSERT…
CHECKED THE INSERTS FOUND VARIATION IN DIFFERENT BATCHES
5.17
5.20
BATCH NO: 3774691 |  | BATCH NO:3791293 |  | BATCH NO:4086935 | 
SL NO | INSERT SPEC | SL NO | INSERT SPEC | SL NO | INSERT SPEC
1 | 4.085 | 1 | 4.124 | 1 | 3.985
2 | 4.083 | 2 | 4.126 | 2 | 3.986
3 | 4.084 | 3 | 4.125 | 3 | 3.986
4 | 4.085 | 4 | 4.126 | 4 | 3.984
5 | 4.085 | 5 | 4.127 | 5 | 3.985
6 | 4.086 | 6 | 4.124 | 6 | 3.985
7 | 4.084 | 7 | 4.124 | 7 | 3.984
8 | 4.086 | 8 | 4.125 | 8 | 3.985
9 | 4.085 | 9 | 4.124 | 9 | 3.986
10 | 4.084 | 10 | 4.125 | 10 | 3.984
5.07
X
X

## Slide 39
INSERT DETAIL
WE NEED TO CHECK THE CURRENT INSERT TOLERENCE
INSERT MANUFACTURING TOLERENCE FOUND MORE THAN THE PART SPEC.
WE NEED AN INSERT HAVING TOLERANCE EQUVALENT TO PART SPEC
Comp spec
X

## Slide 40
TAKEN TRIALS WITH THE GROUND INSERT – LIFE NOT ACHIEVED .
PRECISION GRIND INSERT WILL NOT IMPROVE THE LIFE SHOULD GO FOR MOULDED INSERT
INSERT TRIAL 1
 | BEFORE | AFTER
CURRENT INSERT | A4G0405M04U04 GUP | DTE400 – 040 T9125
TOLERANCE | ± 0.08 | ± 0.020
SET LIFE | 500 | 500
ACTUAL LIFE | 500 | 20 / 30
CUTTING SPEED | 120 | 120
FEED | 0.12 | 0.12
MAKE | KENNAMETAL | TUNGALOY
Chart: TOOL LIFE
| TARGET | ACTUAL
 | 500 | 30
WE NEED THE PRECISSION GRIND INSERT HAVING ±0.020 TOLERENCE FOR THIS APPLICATION
DTE400-040 –GROUND
TOLERANCE ±0.02
X

## Slide 41
ARRANGED 3 BATCH INSERT FOR THE WIDTH VERIFICATION .
THE MAXIMUM VARRAITION COMING IS 0.008 MM
DECIDED TO GO WITH THIS INSERT FOR FURTHER TRIALS .
INSERT SELECTION
CHECKED FOR THE MOULDED INSERT WITH LEAST TOLERANCE
SELECTED GDM4020N-040 GM HAVING TOLERANCE OF ± 0.03 MM
BATCH NO: R0529E4 |  | BATCH NO:R1033EZ |  | BATCH NO: N113905 | 
SL NO | INSERT SPEC | SL NO | INSERT SPEC | SL NO | INSERT SPEC
1 | 3.971 | 1 | 3.970 | 1 | 3.975
2 | 3.975 | 2 | 3.967 | 2 | 3.975
3 | 3.973 | 3 | 3.970 | 3 | 3.970
4 | 3.971 | 4 | 3.974 | 4 | 3.971
5 | 3.974 | 5 | 3.973 | 5 | 3.968
6 | 3.969 | 6 | 3.972 | 6 | 3.973
7 | 3.971 | 7 | 3.973 | 7 | 3.974
8 | 3.975 | 8 | 3.969 | 8 | 3.970
9 | 3.973 | 9 | 3.967 | 9 | 3.968
10 | 3.971 | 10 | 3.967 | 10 | 3.975
GDM4020N-040 GM
TOLERANCE ±0.03

## Slide 42
Chart: FORK TIGHT
| Nov 1W | Nov 2W | Nov 3W | Nov 4W | Dec1W
 | 27 | 32 | 28 | 10 | 13
Chart: TOOL LIFE
| TARGET | ACTUAL
 | 500 | 700
TRIAL SUCCESSFUL AND TOOL LIFE SET TO 700 NOS.
FORK TIGHT REWORK REDUCED . .
INSERT TRIAL 2
Cp & Cpk
 | BEFORE | AFTER
CURRENT INSERT | A4G0405M04U04 GUP | GDM 4020N -040GM
TOLERANCE | ± 0.08 | ± 0.03
SET LIFE | 500 | 500
ACTUAL LIFE | 500 | 700
CUTTING SPEED | 120 | 130
FEED | 0.12 | 0.15
MAKE | KENNAMETAL | KYOCERA
BEFORE
AFTER
INSERT WEAR FOUND OK
Rz 11.45
Chart: TOOL LIFE ESTABLISHMENT
| T1 | T2 | T3
LIFE | 805 | 876 | 856
SET LIFE | 700 | 700 | 700
RZ | 11.17 | 11.58 | 11.55
SPEC: ≤ 12.5
CP1.44 & CPK1.38

## Slide 43
WE COMPLETED OUR ACTIVITY AS PER THE PLAN
Activity schedule plan
MIQC NAME: THE TEAM HORIZON
PROJECT;- FORK TIGHT REWORK ELIMINATION
Meeting time every Friday 3 to 4 pm
DEPT; KAIZEN TEAM
FACILITATER;- KOHJI SAN
START MONTH;- OCT
END MONTH;- NOV
NO OF PROJECTS COMPLETED;-1
MEMBERS
1.SAJIN SAN
2.PRAVEEN SAN
3.MANOHAR SAN
4. PRAMOD SAN
5. DARSHAN SAN

## Slide 44
EFFECT CONFIRMATION

## Slide 45
Chart: M-3 FORK TIGHT REWORK QTY
| 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101
 | 475 | 467 | 576 | 524 | 632 | 905 | 97 | 43 | 3
 | 237.5 | 233.5 | 288 | 262 | 316 | 452.5 | 48.5 | 21.5 | 1.5
Effect confirmation
REWORK REDUCTION
AFTER IMPLEMENTATION FORK TIGHT QUANTITY IS REDUCED
ACHIEVEMENT 99.4%

## Slide 46
HORIZONTAL DIPLOYMENT COMPLETED IN C-4 KTE/K67, C-3 K55 & M-4 K55 LINE
HORIZONTAL DEPLOYMENT

## Slide 47
Chart: REWORK COST
| 42948 | 42979 | 43009 | 43040 | 43070 | 43101
 | 524 | 632 | 905 | 97 | 43 | 3
 | 742.3333 | 895.3333 | 1282.0833 | 137.4167 | 60.9167 | 4.25
Chart: REWORK TIME IN MINUTES/MONTH
| BEFORE | AFTER
 | 267 | 1.5
Tangible benefits
TOOL LIFE UP
REWORK TIME REDUCED
Chart: TOOL LIFE
| TARGET | ACTUAL
 | 200 | 700
Chart: COST SAVING DETAILS
| BEFORE | AFTER | SAVING
 | 171686.1714
 | 296193.4 | 171686.1714 | 124507.2286

## Slide 48
Before Project
After project
intangible benefits
Chart: 
| TEAM WORK | PROBLEM SOLVING | ANALYTICAL ABILITY | QUALITY CONCERN | QC TOOLS
TARGET | 5 | 5 | 5 | 5 | 5
PLAN | 4 | 4 | 4 | 4 | 4
Chart: 
| TEAM WORK | PROBLEM SOLVING | ANALYTICAL ABILITY | QUALITY CONCERN | QC TOOLS
TARGET | 5 | 5 | 5 | 5 | 5
ACTUAL | 5 | 3 | 3 | 4 | 3
TEAM SKILL LEVEL

## Slide 49
Brain storming
Cause and Effect Diagram
We used following QC tools & Techniques to our project
Why-why analysis
QC TOOLS & TECHNICS USED
Pareto Diagram
Process Flow Diagram

## Slide 50
LEARNINGS FROM OUR PROJECT
INSERT SELECTION
PROBLEM ANALYSIS
OPTIMISATION OF CUTTING PARAMETERS
USAGE OF QC TOOLS

## Slide 51
THANK YOU
ANY SUGGESTION PLEASE