## Slide 1
MUSASHI AUTO PARTS INDIA PVT LIMITED
BANGALORE PLANT
FLAME FIGHTING FORGERS
CIRCLE NAME: FLAME FIGHTERS

## Slide 2
MAP-ID IS SITUATED IN BENGALURU KARNATAKA.
WE PROCESS FORGINGS, PERFORM MACHINING, HEAT TREATMENT & ASSEMBLY OF CON RODS, CAM SHAFTS, GEARS & SHAFTS
QUALITY CIRCLE
INTRODUCTION TO OUR COMPANY

## Slide 3
TEAM INRTODUCTION
TEAM LEADER
NAME : SIVAKUMAR SAN
DEPT : PROD- HF
TEAM MEMBER
NAME : MANJUNATH REDDY
DEPT : PROD- HF
TEAM MEMBER
NAME : ANJANEYA SAN
DEPT : PROD- HF
TEAM MEMBER
NAME : THIMMAPPA SAN
DEPT : HOT FORGING
ADVISOR
NAME : SAJIN SAN
FLAME FIGHTERS
TEAM MEMBER
NAME : SARAVANAN SAN
DEPT : HOT FORGING

## Slide 4: FORGING DIE SETTING PART REJECTION REDUCTION
THEME AND TARGET
FROM 0.45% TO 0.2%
THEME
TARGET

## Slide 5
PROBLEM SELECTION BY KJ METHOD
BY KJ METHOD “ FORGING OPERATION ” SELECTED

## Slide 6
PROBLEM SELECTION BY KJ METHOD
BY KJ METHOD “LOAD SETTING REJECTION” PROBLEM POINTS SELECTED.

## Slide 7
ACTIVITY PLAN
Sl No | Methodology Steps | Responsibility | P / A | FY 2018-19 |  |  |  |  |  |  |  |  |  | 
 |  |  |  | DECEMBER 18 |  |  | JANUARY 19 |  |  | FEBRUARY 19 |  |  | MARCH 19 | 
1 | FORMATION OF TEAM | SIVAKUMAR SAN | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
2 | CIRCLE MEETING (1/MONTH) | CIRCLE MEMBERS | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
2 | ANALYSIS OF THE PROBLEM | SIVAKUMAR SAN | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
3 | TARGET SETTING | SIVAKUMAR SAN | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
4 | PRESENT CONDITION ANALYSIS | MANJUNATH REDDY SAN | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
5 | IDEA GENERATION | CIRCLE MEMBERS | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
6 | FEASABILITY STUDY | MANJUNATH REDDY SAN | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
7 | TRAIL IMPLEMENTATION AND CHECKING PERFORMANCE | CIRCLE MEMBERS | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
8 | EFFECTIVENESS CHECK AND COUNTER MEASURE | SIVAKUMAR SAN | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 
9 | FOLLOW UP / REVIEW & RECURRENCE PREVENTION AND DOCUMENTATION , SUSTAIN | SIVAKUMAR SAN | PLAN |  |  |  |  |  |  |  |  |  |  | 
 |  |  | ACTUAL |  |  |  |  |  |  |  |  |  |  | 

## Slide 8
Chart: PART WISE JUNE’18 TO NOV’18 REJ %
| K55 M2 | K55 M3 | K55 M4 | K55 C1 | K55 C3 | K55 C4 | K55G PKS | K55G RS | KTEM M2 | KTEM M3 | KTEM M4 | KTEM C3 | KTEM C4 | KTEN PKS | KTEN RS | K67 M3 | K67 M4 | K67 C3 | K67 C4
REJ % | 0.43581 | 0.3473 | 0.57546 | 0.45409 | 0.26444 | 0.30255 | 0.45735 | 0.55404 | 0.55409 | 0.46181 | 0.4365 | 0.35473 | 0.50049 | 0.46639 | 0.19901 | 0.43151 | 0.29857 | 0.28798 | 0.33643
K55 M4 CONTRIBUTED MORE REJECTION PERCENTAGE IN SETTING REJECTION
BACKGROUND ANALYSIS
JUNE -18 TO NOVEMBER-18 MONTH WISE REJECTION
JUNE -18 TO NOVEMBER-18 PART WISE REJECTION
Chart: MONTH WISE SETTING PART REJECTION IN %
| 43252 | 43282 | 43313 | 43344 | 43374 | 43405
% | 0.39705 | 0.40798 | 0.38973 | 0.38066 | 0.4835 | 0.62328

## Slide 9: # KAIZEN POINT 1
UPSETTER PARTS REJECTION REDUCTION

## Slide 10
BY THIS ANALYSIS FOUND MAJOR CAUSES IS UPSETTER MASTER SAMPLE NOT AVAILABLE SO 3 OR 4 UPSETTER PARTS GETTING REJECTED EVERY DIE SET UP
CAUSE ANALYSIS
LOAD
IMPACT LOAD
MORE UPSETTER REJECTION
MAN
METHOD
MATERIAL
ENVIRONMENT
MACHINE
DUST
BILLET SCALES
WRONG LOAD INDICATION
IMPROPER LUBRICATION
BILLET WEIGHT OVER SIZE
DIES WORNOUT
TOP UPSETTER DIE ADJUSTMENT NOT DONE
BILLET NOT KEPT CENTER OF THE DIE
DIE FITTING
EVERY DIE DIFFERENT HEIGHT
DIES NOT FULLY TIGHTED
DIE WAVENESS
MASTER SAMPLE NOT AVAILABLE
RAM STROKE VARIATION
CAUSE ANALYSIS FOR MORE UPSETTER REJECTION DURING LOAD SETTING

## Slide 11
CURRENT CONDITION
VVV
TOP DIE
BOT DIE
VVV
HOT BILLET
UPSETTER DIAMETER MORE/LESS THAN REQUIRED DIAMETER (REJECTED)
K55 M4 PART REQUIRED UPSETTER DIAMETER IS 47 MM TO 47.5MM BUT ACTUAL PRODUCED DIAMETER MORE THAN OR LESS THAN REQUIRED DIAMETER SO THIS UPSETTER GETS REJECTED. AGAIN TOP DIE ADJUSTMENT REQUIRED UNTILL PRODUCE REQUIRED UPSETTER DIAMTER.
UPSETTER
STEP 1
STEP 1
STEP 1
STEP 4
VVV
AFTER UPSETTER TOP DIE ADJUSTMENT
(OK)

## Slide 12
IMPROVEMENT IDEA
VVV
VVV
TOP DIE
BOT DIE
HOT BILLET
MINIMIZED (3 - 4 NOS TO 1-2 NOS) UPSETTER REJECTION
MADE UPSETTER MASTER SAMPLE ACCORDING REQUIRED DIAMETER
UPSETTER DIE ADJUSTMENT DONE BY USING MASTER SAMPLE
MINIMIZED UPSETTER REJECTION 3- 4 NOS IN TO 1 – 2 NOS.
MASTER 47-47.5MM
VVV
UPSETTER PART PRODUCED AS PER SAMPLE 47-47.5mm
TOP UPSETTER ADJUSTMENT DONE BY USING MASTER SAMPLE
STEP 1
STEP 2
STEP 3
STEP 4

## Slide 13: # KAIZEN POINT 2
UNDERFILL PARTS REJECTION REDUCTION

## Slide 14
FOUND MAJOR CAUSES THAT IS THERE IS NO ANY STANDARD FOR SLIDE ADJUSTMENT AFTER FINISHER DIES CHANGES
CAUSE ANALYSIS
LOAD
IMPACT LOAD
MORE UNDERFILL REJECTION
MAN
METHOD
MATERIAL
ENVIRONMENT
MACHINE
DUST
BILLET SCALES
WRONG LOAD INDICATION
IMPROPER LUBRICATION
BILLET WEIGHT OVER SIZE
DIES WORNOUT
TOP UPSETTER DIE ADJUSTMENT NOT DONE
BILLET NOT KEPT CENTER OF THE DIE
SETTING
EVERY DIE DIFFERENT HEIGHT
DIES NOT FULLY TIGHTED
THERE IS NO STANDARD FOR SLIDE ADJUSTMENT AFTER DIE CHANGE
DIE WAVENESS
NO MASTER SAMPLE
RAM STROKE VARIATION
CAUSE ANALYSIS FOR MORE UNDERFILL REJECTION DURING LOAD SETTING

## Slide 15
CURRENT CONDITION
UPSETTER OK
FIRST STAGE UPSETTER PART OK
BUT SECOND STAGE FINISHER PART FOUND UNDERFILL(REJECTED) DURING LOAD SETTING (NEW DIE SETTING)
BASED ON PREVIOUS PART UNDERFILL PERCENTAGE AGAIN ADJUSTING SLIDE HEIGHT THEN ONE MORE BILLET USING FOR LOAD SETTING MAY BE THIS PART ALSO GETS REJECTED REASON OF UNDERFILL.
LIKE THIS 3-4 PARTS GETTING REJECTED IN THE REASON OF UNDERFILL
REASON NO STANDARDS AVAILABALE FOR SLIDE HEIGHT ADJUSTMENT AFTER DIE CHANGE

## Slide 16: DIFFERENCE VALUE 428.94 FOUND CONSTAND GAP FOR SLIDE HEIGHT AND TOTAL DIE HEIGHT
IMPROVEMENT IDEA
BEFORE MAKING TRIAL PART DIRECTLY SLIDE ADJUSTMENT DONE BY USING ABOVE CALCULATION, SO DIE LOAD SETTING REJECTION MINIMIZED 4 TO 2 NOS
 |  | VARIABLES |  |  | CONSTANT |  |  |  |  | KAIZEN IDEA |  | RESULT
 | PART NAME | TOP DIE HEIGHT | BOTTOM DIE HEIGHT | SLIDE HEIGHT | UPSETTER DIAMETER | UPSETTER THICKNESS | REQ LOAD (220-240T) | KO PIN LEVEL | CASE | (TOTAL HEIGHT) TOP+BOT | DIFFERENCE (TOTAL DIE HEIGHT-SLIDE HEIGHT) | PARTS REJECTED DUE TO UNDERFILL
1ST TIME DIE CHANGE | K55 M4 | 63.2 | 107.06 | 599.2 | 47.2/47.7 | 15.5/15.9 | 230 | 0.5 | 13 | 170.26 | 428.94 | 5
2ND TIME DIE CHANGE | K55 M4 | 62.7 | 106.8 | ? | 47.1/47.5 | 15.5/15.8 | 230 | 0.5 | 13 | 169.5 |  | 2
 |  | VARIABLES |  |  | CONSTANT |  |  |  |  | KAIZEN IDEA |  | RESULT
 | PART NAME | TOP DIE HEIGHT | BOTTOM DIE HEIGHT | SLIDE HEIGHT | UPSETTER DIAMETER | UPSETTER THICKNESS | REQ LOAD (220-240T) | KO PIN LEVEL | CASE | (TOTAL HEIGHT) TOP+BOT | DIFFERENCE (TOTAL DIE HEIGHT-SLIDE HEIGHT) | PARTS REJECTED DUE TO UNDERFILL
1ST TIME DIE CHANGE | K55 M4 | 63.2 | 107.06 | 599.2 | 47.1/47.5 | 15.5/15.9 | 230 | 0.5 | 13 | 170.26 | 428.94 | 5
428.94 + 169.5 = 598.44
SLIDE HEIGHT SETTED WITHOUT ANY PART REJECTED

## Slide 17
RESULT
42 NOS SAVED PER DAY
DESCRIPTIONS | BEFORE | AFTER
REJECTED QTY FOR 1 DIE SETTING | 5 NOS | 3 NOS
EACH SHIFT AVERAGE DIE CHAGING FREQUENCY | 3 TIMES | 3 TIMES
EACH SHIFT TOTAL REJECTION | 15 NOS | 9 NOS
PER PRESS | 15*3=45 NOS | 6*3=27 NOS
HF1 & HF2 PRESS | 45+45=90 NOS | 27+27=52 NOS
Chart: PER DAY REJECTION
| BEFORE | AFTER
 | 90 | 52

## Slide 18
THANK YOU