## Slide 1
K0NA MODEL SPC
Part name | S.R. No | OPT | Control Item | Specification | Cp PP-1 | Class |  | Remarks | Cp PP-2 | Class | Remarks
CAM SHAFT | 1 | Facing cantering | Length | 30.65~30.35 | 1.70 | S |  | OK | 1.71 | S | OK
 | 2 | Facing cantering | Face R/O | 0.05 | 2.27 | S |  | OK | 2.33 | S | OK
 | 3 | Facing centering | Total face R/O | 0.05 | 1.54 | A |  | OK | 1.50 | A | OK
 | 4 | Turning -1 | Diameter | 20.37~20.4 | 1.87 | S |  | OK | 2.11 | S | OK
 | 5 | Turning -1 | Diameter | 19.94~19.91 | 1.47 | A |  | OK | 1.60 | A | OK
 | 6 | Turning -1 | OD R/O | 0.05 | 1.68 | S |  | OK | 1.69 | S | OK
 | 7 | Turning -2 | Diameter | 10.21~10.24 | 1.34 | A |  | OK | 1.46 | A | OK
 | 8 | Turning -2 | OD R/O | 0.05 | 1.37 | A |  | OK | 1.53 | A | OK
 | 9 | DRILLING, REAMING &TAPPING | DIAMETER (REAMING) | 9.65~ 9.980 | 1.39 | A |  | OK | 1.53 | A | OK
 | 10 | DRILLING, REAMING &TAPPING | REAMING DEPTH | 4.5~ 4.7 | 1.66 | A |  | OK | 1.55 | A | OK
SUMMARY OF SPC STUDY- FOR PP1 & PP-2 EVENT
1/5
SPC Study Done for Cam Shaft wise & all Dimension are in S & A Rank.

## Slide 2
K0NA MODEL SPC
SUMMARY OF SPC STUDY- FOR PP1 EVENT
2/5

## Slide 3
KONA MODEL SPC
SUMMARY OF SPC STUDY- FOR PP1 & PP-2 EVENT
3/5
SPC Study Done for Cam Shaft wise & all Dimension are in A Rank.
Part name | S.R. No | OPT | Control Item | Specification | Cp PP-1 | Class | Remarks | Cp PP-2 | Class | Remarks
CAM SHAFT | 11 | DRILLING, REAMING &TAPPING | CONCENTRICITY | 0.1 | 1.53 | A | OK | 1.48 | A | OK
 | 12 | CAM MILLING | CAM IN DIAMETER | 32.543 ±0.04 | 1.61 | A | OK | 1.66 | A | OK
 | 13 | CAM MILLING | CAM EX DIAMETER | 32.613 ±0.04 | 1.44 | A | OK | 1.48 | A | OK
 | 14 | CAM MILLING | PARELLELISM IN & EX CAM | ≤0.05 | 1.55 | A | OK | 1.68 | A | OK
 | 15 | GRINDING | AXIS GRINDING | Ø 10.0 +0.015 +0.006 | 1.44 | A | OK | 1.42 | A | OK
 | 16 | GRINDING | AXIS GRINDING | Ø 20.0 +0.021/ +0.008 | 1.51 | A | OK | 1.40 | A | OK
 | 17 | GRINDING | AXIS GRINDING | Ø 19.8 -0.2 | 1.36 | A | OK | 1.42 | A | OK
 | 18 | CAM GRINDING | CAM IN DIAMETER | Ø 32.048±0.03 | 1.57 | A | OK | 1.63 | A | OK
 | 19 | CAM GRINDING | CAM EX DIAMETER | Ø 32.118±0.03 | 1.35 | A | OK | 1.46 | A | OK
 | 20 | CAM GRINDING | B.C.D. R/O IN &EX-CAM GRINDING | ≤ 0.020 | 1.41 | A | OK | 1.46 | A | OK

## Slide 4
4/5

## Slide 5
SUMMARY OF SPC STUDY- FOR PP-1 & PP-2 EVENT
Part name | S.R. No | OPT | Control Item | Specification | Cp PP-1 | Class | Remark | Cp PP-2 | Class | Remarks
CAM SHAFT | 21 | CAM LAPPING | CAM IN DIA. | 32.043±0.03 | 1.61 | A | OK | 1.48 | A | OK
 | 22 | CAM LAPPING | CAM EX DIA. | 32.113±0.03 | 1.35 | A | OK | 1.46 | A | OK
SPC Study Done for Cam shaft all Dimension are in A Rank.
K0NA MODEL SPC
5/5