## Slide 1
Reamer Operation Missed–K0PG SHAFT COMP CAM
DOWEL COMES OUT WHILE NOISE VEHICLES INSPECTION AT CUSTOMER
MAP-ID BLR
REPORTING DATE: 19th Jan-2022

## Slide 2: REPORT INDEX
Date ： 2021/Dec/10
Reported ： Musashi Auto Parts India Pvt. Ltd
Approval
Check
Issued
Subject ：- DOWEL COMES OUT WHILE NOISE VEHICLES INSPECTION AT CUSTOMER
■Contents of report-Reamer Operation Missed-K0PG Cam Shaft |  |  | 
 | Contents | page | Cum Time Sec
1 | Overview & Background | 01 | 30
2 | Observation & Process Flow | 01 | 30
3 | Traceability | 01 | 30
4 | Identify Occurrence Root cause | 01 | 30
5 | Identify Outflow Root cause | 01 | 30
6 | Occurrence & Outflow Countermeasure | 02 | 60
7 | Standardization | 01 | 30
8 | Countermeasures Summary (With Management action) | 01 | 60
9 | Horizontal deployment | 01 | 30
 | Total(Q & A) | 10 | 5min 30
□ HONDA ACTIVA 6g
Ujjal /Abidali
Hishikari / Prashanth San
Umashankar San
Shaft Comp Cam

## Slide 3: OVERVIEW & BACKGROUND
1. Overview | Parts Name : Shaft comp Cam (K0PG)
1-1. Phenomenon of Occurrence | Reamer Operation Missed
1-2. Number of Claims | 02Nos (Vehicle rolled out)
1-3.Occurance Lot No. | Invoice No. 8212104605
1-4. Cause of Occurrence | Dowel Pin Came Out
1-4. Countermeasure Details | Immediate action: 100% Parts checked Identify Process Verify-Occurrence and Outflow
1-5. Affected Range | 8065Nos
Groove
Groove
Reference photo for understand Problem.
Reamer Operation Missed Parts Having Chamfer Length more
Spe:10.00-0.02 /-0.035mm
( Obs: 9.626 & 9.596mm)
Reamer Operation Parts Having Chamfer Length Less Spe: 10.00-0.02 /-0.035mm
( Obs: 9.975mm)
Available Parts Segregation Details- Shaft Comp Cam Operation Missed |  |  |  |  | 
Sl. No. | Stage | Qty | OK | NG | Pending
1 | Wear house | 15,300 | 15,300 | 0 | 0
2 | FG | 0 | 0 | 0 | 0
3 | QGATE | 0 | 0 | 0 | 0
4 | ASSY | 288 | 288 | 0 | 0
5 | PROCESS | 7777 | 7777 | 0 | 0
Total |  | 23,365 | 23,365 | 0 | 0

## Slide 4: OBSERVATION & PROCESS FLOW
SL No | Verification Items | Rule | Observation On NG Parts | Result
01 | Parts inspection | Parts marking on face after inspection | Available on parts | OK
02 | Dowel Condition | As per drawing | Assy at vehicle there is no any information initially | OK
03 |  | Should not Comes Out | Dowel Pin Comes Out | NG
04 | Initial observation | As per Parameters checked | Cam Shaft ID 10.0 -0.020,0.035 observed up to 9.626 & 9.596 | NG
PROCESS SEQUENCE
DETAILS OF NG PARTS –AS INFORMATION
Induction Hardening
Cam Milling
Keyway Milling
Drilling reaming
Child Parts Assy
Big Bearing Assy
Receiving Inspection
Facing & Centering
Turning 1
Turning 2
Buffing
Small Hole Drilling Reaming
Cam Grinding
Axis Grinding
Cam Lapping
Visual Inspection
Occurrence
Small Bearing Assy
As per the Observation There is control at Occurrence and outflow
Dowel Pin Assy
Final Inspection
Dispatch
Outflow
PRESENT CONTROL AT MAP-ID
ASSEMBLY PROCESS
Occurrence – Under Analysis
LINE-3
LINE-4
LINE-6
LINE-7
K0PG LINES
K0PG ASSY LINES
LINE-2
LINE-3
CONTROLS
Dowel Pin Assy
In load cell identified the Reamer Operation missed parts as NG
Outflow-Controls
Interlock Gauge Pass NG

## Slide 5: CAM SHAFT K0P LOT TRACEABILITY - REAMER OPERATION MISSED
Summary -Observation
1.Supected Batch Dispatch From M/S MAP-ID to M/S MAP-ID GUJRAT On 27.11.2021 on A shift.
2.Supected Defect parts lot Nos 1.10812570 ,10443050 & 10443002 .
3.Total Qty of the Batches 10812570-9811,10443050-2278 10443002-825Nos
4. 4.Defect Parts Made between 23th Nov "C" shift to 26th Nov "C" Shift
5.There is observed one changepoint as per the log book records
xxxxxxxx | Suspected lot Dispatches in the invoice
xxxxxxxx | Defect Parts Flow Lot No.in the Invoice
xxxxxxxx | Not Dispatch in the Invoice.
Line-6
(Checking the points of change)
Robo Drilling
Change point found in Robo Drilling M/C (Tapp Rigid Alarm at Line-6) 2021.11.26 C-shift M/C interrupted.

## Slide 6: OCCURANCE ANALYSIS
4M | PARAMETERS | CHECKING METHOD | ACTUAL | STATUS
M (Man) | Skilled Operator at critical stations Skill of inspector at Q check gate | - Attendance records - Manpower fixation sheet - Skill matrix - Judgement skills | No Change | ○
M ( Machine ) | Change in Machine Change in machine program Major breakdown /maintenance Wear parts condition | -Maintenance records -All Poke-yoke implementation & controls of machine -Change point control/ Log book | With reference to logbook, there is tap rigid alarm in line 6 | X
M (Method ) | - As per PQCS As per work instruction As per rules | -PQCS revision -Work instructions -Rule root/procedure Vs Actual (By check sheet/record) | NG Parts Outflow to Next Process | X
M (Material ) | As per PQCS Change in Sub supplier | -PQCS -Approved sub supplier list | No Change | ○
CHANGE POINT RECORD
In line 6 Logbook Record there is change point in Machine Alarm on the day
Logbook Sheet
Rejection Logbook Sheet

## Slide 7: IDENTIFY OCCURRENCE ROOT CAUSE
REAMER MISSED WHY WHY ANALYSIS
Step | Why1 | Why2 | Why3 | Why4 | Why5
Occurrence | Cutting sequence as per program one tool missed | Tap rigid alarm | Excess load on spindle during tap | Clamped Part slipped due to Clamping jaws worn out | Premature failure of Jaws
 | Treated as normal part | By Visual check took decision | Self Judgment taken with Visual Inspection (OK Method: Plug Gauge) | Misjudged as Alarm was regarding Tapping and thread was present and OK in the part | Less awareness on the judgement procedure after alarm
Reamer Missed Factor Analysis
Sl No | Possible causes | Rule | Actual | Status
1 | Tool condition | No breakage | No Damage | O
2 | Power failure | Follow Power Failure handling Rules | No Power Failure | O
3 | Machine Interruption | Cutting has to be done as per the program sequence | Incomplete cutting sequence ( Rigid tap alarm) | X
4 | Inspection Frequency | 1/50 measuring frequency | Frequency followed | O
5 | Alarm Parts Handling | Treat as abnormal part | Treated as normal part | X
6 | Setup Change | No mix up of abnormal part | No mix up (No setup change) | O

## Slide 8: OCCURRENCE & OUTFLOW MECHANISM
Overall process
Facing and centering
Turning 1
Turning 2
Drilling,tapping,reaming
Keyway milling
Cam milling
Induction hardening
Occurrence & Outflow
Outflow
Occurrence
Drilling
Tapping
Reaming
Change Point
Simulation Part
Customer simulation Information
Conclusion:-Since the simulation, the cause of the reamer operation miss is parts tilled due to less gripper
Change Point
In robo drill machine tap rigid alarm coming
Scrap Not Highlight no evidence on Scrap
Conclusion-Outflow to next process
Parts handling
Axis grinding
Cam grinding
Small hole drilling reaming
Buffing
Cam lapping
Visual inspection
After alarm part coming in inspection chute
In logbook two part rejected in robo drill operation
Clamping jaw face line mark coming in jaws face
Part clamping condition
Thread operation completed part
Reamer not ok dimensions 9.625mm (specification 9.965mm-9.980mm) operation checking
Inspect by manually
Load the part by manually
Next operation no detection reamer operation
Conclusion:- Based on the simulation cause of the reamer operation miss due to part slippage issue. After tap change no alarm found.

## Slide 9: OCCURRENCE COUNTERMEASURE-PROCESS
Occurrence
Before
After
Outflow
Before
After-Proposal
Jaw Gripper Under
process
Pin Type Sensor mounting to identify Operation
Φ9.9
Conclusion:- 1.Clamping pad changed for better clamping & detection pokayoke Feasibility under discussion with machine maker.
POKA YOKE Drawing
New Metal Clamping.
Jaw Gripper Under
process
Brass clamping pad.
Feasibility is under discussion with machine maker
Life established: 1,00,000 pices.
Obs: 82,000
Life established: monitoring is started.

## Slide 10
TPM CHECK SHEET ( Evidence requested by customer )
Fixture condition Visual inspection check point available in TPM.

## Slide 11
FIXTURE LIFE CONTROL ( Evidence requested by customer )
Macro program is crated for life monitoring.

## Slide 12: ANALYSIS-4M OUTFLOW
4M | PARAMETERS | CHECKING METHOD | ACTUAL | STATUS
M (Man) | Skilled Operator at critical stations Skill of inspector at Q check gate | - Attendance records - Manpower fixation sheet - Skill matrix - Judgement skills | No Change | ○
M ( Machine ) | Change in Machine Change in machine program Major breakdown /maintenance Wear parts condition | -Maintenance records -All Poke-yoke implementation & controls of machine -Change point control/ Log book | No Change | ○
M (Method ) | - As per PQCS As per work instruction As per rules | -PQCS revision -Work instructions -Rule root/procedure Vs Actual (By check sheet/record) | NG Parts Outflow to Next Process | x
M (Material ) | As per PQCS Change in Sub supplier | -PQCS -Approved sub supplier list | No Change | ○
CHANGE POINT RECORD
As per The Logbook Record there is a change point in 26.11.2021 C-shift M/C got interrupted

## Slide 13: IDENTIFY OUTFLOW ROOT CAUSE
Factor analysis :
Sl No | Possible causes | Rule | Actual | Status
1 | Load Cell Working Condition | No abnormal | No abnormal | O
2 | Operator Skill | Skill level2 (Individual can Operate) | Person is Skilled(Level-2) | O
3. | Alarm (NG) Parts Handling | Followed as per NG part Handling rule with QTAR | Followed with QTAR, but couldn’t capture the Reamer miss part | X
4. | Gauge Detection | Gauge detect as NG | Gauge detected as NG | O
Outflow Why Why :
Step | Why1 | Why2 | Why3 | Why4 | Why5
Occurrence | Alarm part handling Followed with QTAR, but couldn’t capture the Reamer miss part | Part found OK as per existing alarm part handling procedure | In Alarm part handling, Once finding OK after Hand press check and Dowel pin height check, part will be passed | Reamer miss possibility not addressed in alarm parts sorting Procedure | With the Confidence of Existing controls and No past trouble history.

## Slide 14: OUTFLOW MECHANISM
ALARM PARTS HANDLING FLOW
OUT FLOW MECHANISM WITH SIMULATION
While Our Inspection of alarm parts Not Consider reamer inside diameter of reamer operation miss parts outflow

## Slide 15: OUTFLOW ACTION
Load NG alarm
Identify the part
Raise QTAR
Keep in Alarm part designated bin
Verify with Hand Press
Verify Dowel height
Pass the part if found OK
Loose
High
Reject the Part
Remove the Dowel pin
Repress
Reject if Already One time Alarm part
Load NG alarm
Identify the part
Raise QTAR
Keep in Alarm part designated bin
Pass the part if found OK
Remove the Dowel pin
Reject if Re Alarm
Verify Reamer Dia and Height
Repress
Reject if NG
BEFORE
AFTER
Reverification without removing
Dowel pin remove and Part Condition Check
Re Inspection of Parameters without removing the dowel pin
Procedure Modify to remove the dowel pin directly and to inspect reaming parameters before re press

## Slide 16: OUTFLOW COUNTERMEASURE
Before-Parts Confirmation
After-Parts Confirmation
Axis Dia Inspection
Big Bearing Pressing
Small Bearing Pressing
Dowel Pin Pressing
Dowel Pin Pressing
+0.01
21
Ø 9.8-0.10
Axis Diameters inspection Gauge
OK
NG-
Reamer Opt Missed
Both Parts Same in the gauge-No Detection
Reamer operation Parts not Qualify in Gauge and machine not start.
+0.01
20
Ø 9.6-0.10
OK & NG
Detection of reamer Operation missed POKA YOKE Initiated, effectiveness and under monitoring
Locator
Snap Gause
Snap Gauge
Interlock With M/C
Locator Pin has modified to detect the NG Parts(Operation Missed)

## Slide 17
OCCURRENCE & OUTFLOW COUNTERMEASURE WITH MANAGEMENT ACTION
 | Root Cause | Activity | In Charge | Target Date | Status
O C C U R A N C E | Premature Failure of Jaws | Life to be Re Established by considering premature failure. 2.Clamping pad is changed from brass to steel. 3.Knurling to be Provided for Existing jaws and same to be standardized in Drawing 4. Alarm resetting procedure readdressed for effectiveness. 5 Feasibility to check for POKA YOKA at Manual Loading table for next process. 6.Reamer dia 100% check before assy for one month period for effectiveness confirmation. | Praveen /Abidali Abidali Abidali Abidali Abidali/Ratheesh San Abidali | 12.01.2022 12.01.2022 14.02.2022 20.12.2021 20.01.2022 On going | O O ∆ O ∆ ∆
O U T F L O W | Less awareness on the judgement procedure after alarm No Past Experience. | Standard procedure modified for alarm Judgement parts Alarm Parts treat as Rejection and put red tag and keep in red bin awareness given to all associate line for the issue. Awareness Given to all associate for the Issue. Rework for the Dowel Alarm parts started as defined QTAR Rule. SOP Made for the Alarm handling Parts. POKA YOKE to be implement to detect while Grinding OD Check | Abidali Abidali Seema Seema Seema Seema | 13.01.2022 17.12.2021 18.12.2021 16.12.2021 20.12.2021 20.12.2021 | O O O O O O

## Slide 18
Standardization
OCCURRENCE
Life Tracking Sheet for Jaws
Jaw Drg Before
Jaw Drg After
Now life monitoring is started for premature of Jaws.
Brass clamping pad
Steel clamping pad
OJT
Alarm Re-Setting Process
Skill Matrix

## Slide 19
Standardization
OUTFLOW
OJT
Updated FMEA
Judgment Procedure
Before
After
Operator check alarm
Operator check alarm
Raise the line siren
Line leader Correct The alarm
Take decision
In case ok part move the next operation or part NG found follow the NG process
SOP
Correct the alarm
Check Parts
Flow to next process by manual loading

## Slide 20
GEMBA EDUCATION & IZIWARU TEST
TV DISPLAY AT ASSY
IZIWARU TEST –ASSOCIATE WISE
Process miss & poka-yoke by video education at gemba & Assy area IZIWARU test conducted.

## Slide 21
HORIZONTAL DEPLOYMENT & MANAGEMENT ACTION
Areas | Countermeasure Horizontal Deployment | Line to be Implement |  |  |  |  |  |  |  | 
 |  | Assy Line-2 | Assy K0NA | Assy K1CA | Line-1 K0NA | Line-2 K0NA | Line-3 K0PG | Line-4 K0PG | Line-5 K1CA | Line-7 K0PG
Occurrence | Life to be Fixed for Clamping pad. | NA | NA | NA | O | O | O | O | O | O
 | Clamp jaws face Knurling to more grip on Part. | NA | NA | NA | NA | NA | O | O | O | O
 | POKA YOKA to be implement at Manual Loading table for next process. | NA | NA | NA | O | O | O | O | NA | O
 | Operator press siren button when received alarm in machine. | NA | NA | NA | O | O | O | O | O | O
Outflow | Standard procedure made for judgment on alarm parts | O | O | O | O | O | O | O | O | O
 | Alarm Parts treat as Rejection and put red tag and keep in red bin awareness given to all associate line for the issue. | O | O | O | O | O | O | O | O | O
 | Awareness Given to all associate for the Issue. | O | O | O | O | O | O | O | O | O
 | Rework for the Dowel Alarm parts started as defined QTAR Rule. | O | O | O |  |  |  |  |  | 
 | SOP Made for the Alarm handling Parts. | O | O | O |  |  |  |  |  | 
 | POKA YOKE to be implement to detect while Grinding OD Check | O | O | O |  |  |  |  |  | 
Actions are initiated and horizontally deployment and will complete within this Month.
1
2
3
4
1
2
3
4
5
6

## Slide 22
THANKS